## Slide 1: Anti-Sway Control of Overhead Cranes
Reinaldo Maslim
Supervisor: Dr. Chen Silu

## Slide 2: About gantry cranes
Used in several industries: ports, steel mills, nuclear power plant, etc.
Can deliver any bulky loads
Controlled manually by operator
Swaying of load decreases productivity, safety, and requires very skillful operator
Swaying motion caused by:
  Acceleration
  External disturbance: wind

## Slide 3: System to be Controlled
Assumptions:
The trolley and payload are regarded as point masses.
Friction force can be neglected.
The length of hoisting rope is time-invariant.
The trolley and load move in a 2D plane.
Practically, the sway angle is small.
Langrangian mechanics

## Slide 4: Control strategies
Time Optimal Control
Feedback Control
Input Shaping (Feedforward)
Bang-Bang
Linear Quadratic Regulator
PID
Precalculated trajectory
Zero Vibration-filter
Gain Scheduling
Genetic algorithm
Fuzzy logic
Artifical Neural Network
Sliding Mode

## Slide 5: Control Strategies
OPEN-loop INput Shaping Method
Adapted from observation of operators:
Accelerate  Sway minimum
Constant velocity  Sway maximum
Accelerate  Speed trolley=speed payload
Repeat to achieve max speed
Reverse maneuver to stop

## Slide 6: Control Strategies
Area under velocity graph= travelled distance. Acceleration profiles can be precalculated.
For optimum time transfer, use maximum acceleration pulses.
Mathematical proof in report.

## Slide 7: Control Strategies
CLOSED-LOOp anti-sway damping factor with sway-angle estimator
Second order without damping:
Modified equation includes damping
for Anti-sway mechanism

## Slide 8: Control Strategies; Adding sway angle feedback term
Conventional PD control in Position and Speed controllers.
K value can be tuned for preferable performance (damping coefficient)

## Slide 9: Control Strategies; using payload position instead of trolley position
CLOSED-LOOp with payload position As feedback

## Slide 10: Testbed Model Design
TABLE 1 |  | 
Parameters | Actual Crane | Model Crane
Trolley mass M | 26 ton | 1.2 kg
Payload mass m | 67.3 ton | 1 kg
Length of hoist rope L | 40 m | 0.6 m
Rated speed of trolley | 3 m/s | 0.5 m/s
Rated acceleration time | 0.5 m/s2 | 0.1 m/s2
Rated power of trolley motor | 110 kW | 232 W
Gravitational acceleration g | 9.81 m/s2 | 9.81 m/s2

## Slide 11: Sway-angle Sensing Verification
Angle verification difficult in testbed because string is used instead of rod.
High resolution sensor 1mm with sufficient feedback frequency.
Sway angle can be obtained as

## Slide 12: Simulation Studies
A delivery task is assigned to all three control schemes.
Transfer load from 0 m to 120 m with average velocity of 3m/s. Parameters used shown in Table 1.

## Slide 13: Simulation Studies; Results of Input shaping
Good performance in indoor environment where no disturbance exist.
Cannot work well when disturbance exist because no feedback.
Suitable for Indoor cranes.

## Slide 14: Simulation Studies; Results of Antisway feedback term
Settling time can be decreased at the cost of higher overshoot.
Able to suppress sway angle even at the presence of wind.

## Slide 15: Simulation Studies; Results of Payload position feedback
Payload’s position tracking to generated trajectory can be guaranteed -> Safety is ensured even in wind’s presence.
Trolley keeps swaying to and fro to compensate for trolleys swaying due to wind or acceleration-induced motion.

## Slide 16: Simulation Studies
Concern:
Velocity of trolley must be set within feasible range of real motors slower trajectoryless favourable.

## Slide 17: Conclusions
All three controllers are able to work with each of their advantages and disadvantages.
A testbed has been developed for further studies.

## Slide 18: Future Works
Include more varying parameters.
Mathematically proof control strategy and stability of closed loop with payload’s position feedback controller.
State observers implemented for real time.
Model-free controllers must be developed.
Integration with Active Heave Compensation(AHC) for offshore cranes.

## Slide 19: Thank you for your attention 
We welcome your questions, suggestions or comments!